## Slide 1
Digital Design and Computer Architecture:
ARM® Edition
Sarah L. Harris and David Money Harris, © 2015, Elsevier
Textbook

## Slide 2
Chapter 1
Digital Design and Computer Architecture: ARM® Edition
Sarah L. Harris and David Money Harris

## Slide 3
Background
The Game Plan
The Art of Managing Complexity
The Digital Abstraction
Number Systems
Logic Gates
Logic Levels
CMOS Transistors
Power Consumption
Chapter 1 :: Topics

## Slide 4
Microprocessors have revolutionized our world
  Cell phones, Internet, rapid advances in medicine, etc.
The semiconductor industry has grown from $21 billion in 1985 to $306 billion in 2015.
Background

## Slide 5
Purpose of course:
Understand what’s under the hood of a computer
Learn the principles of digital design
Learn to systematically debug increasingly complex designs
Design and build a microprocessor
The Game Plan

## Slide 6
Abstraction
Discipline
The Three –y’s
  Hierarchy
  Modularity
  Regularity
The Art of Managing Complexity

## Slide 7
Hiding details when they aren’t important
Abstraction
Increasing Abstraction

## Slide 8
Intentionally restrict design choices
Example: Digital discipline
  Discrete voltages instead of continuous
  Simpler to design than analog circuits – can build more sophisticated systems
  Digital systems replacing analog predecessors: i.e., digital cameras, digital television, cell phones, CDs
Discipline

## Slide 9
The Three -y’s
Hierarchy
Modularity
Regularity

## Slide 10
Hierarchy
  A system divided into modules and submodules
Modularity
  Having well-defined functions and interfaces
Regularity
  Encouraging uniformity, so modules can be easily reused
The Three -y’s

## Slide 11
Hierarchy
  Three main modules: lock, stock, and barrel
  Submodules of lock: hammer, flint, frizzen, etc.
Example: The Flintlock Rifle

## Slide 12
Modularity
  Function of stock: mount barrel and lock
  Interface of stock: length and location of mounting pins
Regularity
  Interchangeable parts
Example: The Flintlock Rifle

## Slide 13
Most physical variables are continuous
  Voltage on a wire
  Frequency of an oscillation
  Position of a mass
Digital abstraction considers discrete subset of values
The Digital Abstraction

## Slide 14
Designed by Charles Babbage from 1834 – 1871
Considered to be the first digital computer
Built from mechanical gears, where each gear represented a discrete value (0-9)
Babbage died before it was finished
The Analytical Engine

## Slide 15
Digital Discipline: Binary Values
Two discrete values:
  1 and 0

## Slide 16
Digital Discipline: Binary Values
Two discrete values:
  1 and 0
  1, TRUE, HIGH
  0, FALSE, LOW
How to represent 1 and 0?

## Slide 17
Digital Discipline: Binary Values
Two discrete values:
  1 and 0
  1, TRUE, HIGH
  0, FALSE, LOW
How to represent 1 and 0? voltage levels, rotating gears, fluid levels, etc.
Digital circuits use voltage levels to represent 1 and 0
Bit: Binary digit

## Slide 18
Why Digital Systems?

## Slide 19
Why Digital Systems?
Easier to design
Fast
Can overcome noise
Error detection/correction

## Slide 20
George Boole, 1815-1864
Born to working class parents
Taught himself mathematics and joined the faculty of Queen’s College in Ireland
Wrote An Investigation of the Laws of Thought (1854)
Introduced binary variables
Introduced the three fundamental logic operations: AND, OR, and NOT

## Slide 21
George Boole, 1815-1864
Born to working class parents
Taught himself mathematics and joined the faculty of Queen’s College in Ireland
Wrote An Investigation of the Laws of Thought (1854)
Introduced binary variables
Introduced the three fundamental logic operations: AND, OR, and NOT

## Slide 22
Number Systems
Decimal
  Base 10
Binary
  Base 2
Hexadecimal
  Base 16

## Slide 23
Decimal Numbers
Base 10 (our everyday number system)
Base 10

## Slide 24
Decimal Numbers
Base 10 (our everyday number system)
Base 10

## Slide 25
Decimal and Binary Numbers
Base 10 (our everyday number system)
Base 2: Binary numbers
Base 2

## Slide 26
Decimal and Binary Numbers
Base 10 (our everyday number system)
Base 2: Binary numbers
Base 2

## Slide 27
20 =
21 =
22 =
23 =
24 =
25 =
26 =
27 =
28 =
29 =
210 =
211 =
212 =
213 =
214 =
215 =
Powers of Two

## Slide 28
20 = 1
21 = 2
22 = 4
23 = 8
24 = 16
25 = 32
26 = 64
27 = 128
28 = 256
29 = 512
210 = 1024
211 = 2048
212 = 4096
213 = 8192
214 = 16384
215 = 32768
Powers of Two
Handy to memorize up to 29

## Slide 29
Binary to decimal conversion:
  Convert 100112 to decimal
Decimal to binary conversion:
  Convert 4710 to binary
Number Conversion

## Slide 30
Binary to decimal conversion:
  Convert 100112 to decimal
  16×1 + 8×0 + 4×0 + 2×1 + 1×1 = 1910
Decimal to binary conversion:
  Convert 4710 to binary
  32×1 + 16×0 + 8×1 + 4×1 + 2×1 + 1×1 = 1011112
Number Conversion

## Slide 31
Two methods:
  Method 1: Find the largest power of 2 that fits, subtract and repeat. (Recommended method)
  Method 2: Repeatedly divide by 2, remainder goes in next most significant bit
Decimal to Binary Conversion

## Slide 32
Decimal to Binary Conversion
  Method 1: Find the largest power of 2 that fits, subtract and repeat.
  5310
Method 2: Repeatedly divide by 2, remainder goes in next most significant bit.
  5310

## Slide 33
Decimal to Binary Conversion
  Method 1: Find the largest power of 2 that fits, subtract and repeat.
  5310 32×1
  53-32 = 21 16×1
  21-16 = 5 4×1
  5-4 = 1 1×1 = 1101012
Method 2: Repeatedly divide by 2, remainder goes in next most significant bit.
  5310 = 53/2 = 26 R1
  26/2 = 13 R0
  13/2 = 6 R1
  6/2 = 3 R0
  3/2 = 1 R1
  1/2 = 0 R1 = 1101012

## Slide 34
  Another example: Convert 7510 to binary.
Decimal to Binary Conversion

## Slide 35
  Another example: Convert 7510 to binary.
  7510= 64 + 8 + 2 + 1 = 10010112
Decimal to Binary Conversion

## Slide 36
  Another example: Convert 7510 to binary.
  7510= 64 + 8 + 2 + 1 = 10010112
or
75/2 = 37 R1
37/2 = 18 R1
18/2 = 9 R0
9/2 = 4 R1
4/2 = 2 R0
2/2 = 1 R0
1/2 = 0 R1
Decimal to Binary Conversion

## Slide 37
Number Conversion
Binary to decimal conversion:
  Convert 111012 to decimal
  16×1 + 8×1 + 4×1 + 2×0 + 1×1 = 2910
Decimal to binary conversion:
  Convert 4710 to binary
  32×1 + 16×0 + 8×1 + 4×1 + 2×1 + 1×1 = 1011112

## Slide 38
N-digit decimal number
  How many values?
  Range?
  Example: 3-digit decimal number:
N-bit binary number
  How many values?
  Range:
  Example: 3-digit binary number:
Binary Values and Range

## Slide 39
N-digit decimal number
  How many values? 10N
  Range? [0, 10N - 1]
  Example: 3-digit decimal number:
    103 = 1000 possible values
    Range: [0, 999]
N-bit binary number
  How many values? 2N
  Range: [0, 2N - 1]
  Example: 3-digit binary number:
    23 = 8 possible values
    Range: [0, 7] = [0002 to 1112]
Binary Values and Range

## Slide 40
Example:
11012 = 1 × 23 + 1 × 22 + 0 × 21 + 1 × 20
= 8 + 4 + 0 + 1
= 13
Binary Numbers

## Slide 41
Hex Digit | Decimal Equivalent | Binary Equivalent
0 | 0 | 
1 | 1 | 
2 | 2 | 
3 | 3 | 
4 | 4 | 
5 | 5 | 
6 | 6 | 
7 | 7 | 
8 | 8 | 
9 | 9 | 
A | 10 | 
B | 11 | 
C | 12 | 
D | 13 | 
E | 14 | 
F | 15 | 
Hexadecimal Numbers

## Slide 42
Hexadecimal Numbers
Hex Digit | Decimal Equivalent | Binary Equivalent
0 | 0 | 0000
1 | 1 | 0001
2 | 2 | 0010
3 | 3 | 0011
4 | 4 | 0100
5 | 5 | 0101
6 | 6 | 0110
7 | 7 | 0111
8 | 8 | 1000
9 | 9 | 1001
A | 10 | 1010
B | 11 | 1011
C | 12 | 1100
D | 13 | 1101
E | 14 | 1110
F | 15 | 1111

## Slide 43
Base 16
Shorthand for binary
Hexadecimal Numbers

## Slide 44
Hexadecimal to Binary Conversion
Hexadecimal to binary conversion:
  Convert 4AF16 (also written 0x4AF) to binary
Hexadecimal to decimal conversion:
  Convert 4AF16 to decimal

## Slide 45
Hexadecimal to Binary Conversion
Hexadecimal to binary conversion:
  Convert 4AF16 (also written 0x4AF) to binary
  0100 1010 11112
Hexadecimal to decimal conversion:
  Convert 4AF16 to decimal
  4 × 162 + A × 161 + F × 160
  4 × 162 + 10 × 161 + 15 × 160 = 119910

## Slide 46
Bits, Bytes, Nibbles…
Bits
  msb: most significant bit
  lsb: least significant bit
Bytes & Nibbles
Bytes
  MSB: most significant byte
  LSB: least significant byte

## Slide 47
Bits, Bytes, Nibbles…
Bits
  msb: most significant bit
  lsb: least significant bit
Bytes & Nibbles
Bytes
  MSB: most significant byte
  LSB: least significant byte
  Each hex digit represents
  a nibble (4 bits)

## Slide 48
Large Powers of Two
210 = 1 kilo ≈ thousand (1024)
220 = 1 mega ≈ million (1,048,576)
230 = 1 giga ≈ billion (1,073,741,824)
240 = 1 tera ≈ trillion (1,099,511,627,776)
250 = 1 peta ≈ 1015
260 = 1 exa ≈ 1018

## Slide 49
Large Powers of Two
210 = 1 kilo (kibi) ≈ 103 (1024)
220 = 1 mega (mebi) ≈ 106 (1,048,576)
230 = 1 giga (gibi) ≈ 109 (1,073,741,824)
240 = 1 tera (tebi) ≈ 1012
250 = 1 peta (pebi) ≈ 1015
260 = 1 exa (exbi) ≈ 1018

## Slide 50
Large Powers of Two
210 = 1 kilo ≈ 1000 (1024)
  kibibyte = 1 Ki
  for example: 1 KiB = 1024 Bytes
  1 Kib = 1024 bits
220 = 1 mega ≈ 1 million (1,048,576)
  mebibyte = 1 Mi
  for example: 1 MiB, 1 Mib (1 megabit)
230 = 1 giga ≈ 1 billion (1,073,741,824)
  gibibyte = 1 Gi
  for example: 1 GiB, 1 Gib

## Slide 51
What is the approximate value of 224?
Approximately how many values can a 32-bit variable represent?
Estimating Powers of Two

## Slide 52
What is the approximate value of 224?
24 × 220 ≈ 16 million
Approximately how many values can a 32-bit variable represent?
22 × 230 ≈ 4 billion
Estimating Powers of Two
First factor out the largest 210x. Then estimate.

## Slide 53
Decimal
Binary
Addition

## Slide 54
Decimal
Binary
Addition

## Slide 55
Add the following 4-bit binary numbers
Add the following 4-bit binary numbers
Binary Addition Examples

## Slide 56
Add the following 4-bit binary numbers
Add the following 4-bit binary numbers
Binary Addition Examples

## Slide 57
The addition of two 4-bit values (inputs) gives a 4-bit result (output).
  Any additional bits on the left are ignored (overflow!)
Generally, addition of two n-bit numbers gives an n-bit result.
Binary Addition: Numbers of Bits
Overflow!

## Slide 58
Digital systems operate on a fixed number of bits
Overflow: when the result is too big to fit in the available number of bits
See previous example of 11 + 6
Overflow
Overflow!

## Slide 59
Sign/Magnitude Numbers
Two’s Complement Numbers
Signed Binary Numbers

## Slide 60
1 sign bit, N-1 magnitude bits
Sign bit is the most significant (left-most) bit
  Positive number: sign bit = 0
  Negative number: sign bit = 1
Example, 4-bit sign/mag representations of ± 6:
+6 =
- 6 =
Range of an N-bit sign/magnitude number:
Sign/Magnitude Numbers

## Slide 61
1 sign bit, N-1 magnitude bits
Sign bit is the most significant (left-most) bit
  Positive number: sign bit = 0
  Negative number: sign bit = 1
Example, 4-bit sign/mag representations of ± 6:
+6 = 0110
- 6 = 1110
Range of an N-bit sign/magnitude number:
[-(2N-1-1), 2N-1-1]
Sign/Magnitude Numbers

## Slide 62
1 sign bit, N-1 magnitude bits
Sign bit is the most significant (left-most) bit
  Positive number: sign bit = 0
  Negative number: sign bit = 1
Example, 4-bit sign/mag representations of ± 6:
+6 = 0110
- 6 = 1110
Range of an N-bit sign/magnitude number:
[-(2N-1-1), 2N-1-1]
Sign/Magnitude Numbers

## Slide 63
Example:
11012 = 1 × 23 + 1 × 22 + 0 × 21 + 1 × 20
= 8 + 4 + 0 + 1
= 13
Unsigned Binary Numbers

## Slide 64
Sign/Magnitude Numbers
Example:
11012 = (-1)1 × (1 × 22 + 0 × 21 + 1 × 20)
= -1 × (4 + 0 + 1)
= -5

## Slide 65
Problems:
Addition doesn’t work, for example -6 + 6:
1110
+ 0110
10100 (wrong!)
Two representations of 0 (± 0):
1000
0000
Sign/Magnitude Numbers

## Slide 66
Don’t have same problems as sign/magnitude numbers:
  Addition works
  Single representation for 0
Two’s Complement Numbers

## Slide 67
Two’s Complement Numbers
Most significant bit (msb) has value of -2N-1
For example, a 4-bit 2’s complement number:

## Slide 68
Two’s Complement Numbers
Most significant bit (msb) has value of -2N-1
For example, a 4-bit 2’s complement number:
Value = -8 + 2 + 1 = -5
(We’ll show another way to find this value in a moment.)

## Slide 69
Two’s Complement Numbers
msb has value of -2N-1
Most positive 4-bit number:
Most negative 4-bit number:
The most significant bit still indicates the sign (1 = negative, 0 = positive)
Range of an N-bit two’s complement number:

## Slide 70
Two’s Complement Numbers
msb has value of -2N-1
Most positive 4-bit number: 0111
Most negative 4-bit number: 1000
The most significant bit still indicates the sign (1 = negative, 0 = positive)
  Range of an N-bit two’s complement number:
  [-(2N-1), 2N-1-1]

## Slide 71
Example:
11012 = 1 × 23 + 1 × 22 + 0 × 21 + 1 × 20
= 8 + 4 + 0 + 1
= 13
Unsigned Binary Numbers

## Slide 72
Two’s Complement Numbers
Example:
11012 = 1 × (-23) + [ 1 × 22 + 0 × 21 + 1 × 20 ]
= -8 + [ 4 + 0 + 1 ]
= -3

## Slide 73
“Taking the Two’s Complement”
Flips the sign of a two’s complement number.
  It makes a positive number negative.
  It makes a negative number positive.
Method:
    Invert the bits
    Add 1

## Slide 74
“Taking the Two’s Complement”
Flips the sign of a two’s complement number.
Method:
    Invert the bits
    Add 1
Example: Flip the sign of 310 = 00112
    1100
    + 1
    1101 = -310

## Slide 75
Take the two’s complement of 610 = 01102
Two’s Complement Examples

## Slide 76
Take the two’s complement of 610 = 01102
    1001
    + 1
    10102 = -610
Two’s Complement Examples

## Slide 77
What is the decimal value of the two’s complement number 10012?
Two’s Complement Examples

## Slide 78
Two’s Complement Examples
What is the decimal value of the two’s complement number 10012?
  We know it’s negative (msb = 1)
  Figure out magnitude by flipping the sign (i.e., “taking the two’s complement”)
    0110
    + 1
    01112 = 710
  So, we know it’s a negative number with magnitude 7.
  Thus, 10012 = -710
  Taking the two’s complement is the second (and recommended) way of figuring out the value of a negative two’s complement number.

## Slide 79
Two’s Complement Addition
Add 6 + (-6) using two’s complement numbers
Add -2 + 3 using two’s complement numbers

## Slide 80
Add 6 + (-6) using two’s complement numbers
Add -2 + 3 using two’s complement numbers
Two’s Complement Addition

## Slide 81
Extend number from N to M bits (M > N) :
  Sign-extension
  Zero-extension
Increasing Bit Width

## Slide 82
Sign bit copied to msb’s
Number value is same
Example 1:
  4-bit representation of 3 = 0011
  8-bit sign-extended value: 00000011
Example 2:
  4-bit representation of -5 = 1011
  8-bit sign-extended value: 11111011
Sign-Extension

## Slide 83
Zeros copied to msb’s
Value changes for negative numbers
Example 1:
  4-bit value = 0011 = 310
  8-bit zero-extended value: 00000011 = 310
Example 2:
  4-bit value = 1011 = -510
  8-bit zero-extended value: 00001011 = 1110
Zero-Extension

## Slide 84
Number System | Range
Unsigned | [0, 2N-1]
Sign/Magnitude | [-(2N-1-1), 2N-1-1]
Two’s Complement | [-2N-1, 2N-1-1]
For example, 4-bit representation:
Number System Comparison

## Slide 85
George Boole, 1815-1864
Born to working class parents
Taught himself mathematics and joined the faculty of Queen’s College in Ireland
Wrote An Investigation of the Laws of Thought (1854)
Introduced binary variables
Introduced the three fundamental logic operations: AND, OR, and NOT

## Slide 86
Perform logic functions:
  inversion (NOT), AND, OR, NAND, NOR, etc.
Single-input:
  NOT gate, buffer
Two-input:
  AND, OR, XOR, NAND, NOR, XNOR
Multiple-input
Logic Gates

## Slide 87
Single-Input Logic Gates

## Slide 88
Single-Input Logic Gates

## Slide 89
Two-Input Logic Gates

## Slide 90
Two-Input Logic Gates

## Slide 91
More Two-Input Logic Gates

## Slide 92
More Two-Input Logic Gates

## Slide 93
Multiple-Input Logic Gates

## Slide 94
Multi-input XOR: Odd parity
Multiple-Input Logic Gates

## Slide 95
Multi-input XOR: Odd parity
Multiple-Input XOR
Multi-input XOR: Odd parity – the output is 1 when an odd number of inputs is 1.

## Slide 96
Discrete voltages represent 1 and 0
For example:
  0 = ground (GND) or 0 volts
  1 = VDD or 5 volts
What about 4.99 volts? Is that a 0 or a 1?
What about 3.2 volts?
Logic Levels

## Slide 97
Range of voltages for 1 and 0
Different ranges for inputs and outputs to allow for noise
Logic Levels

## Slide 98
What is Noise?

## Slide 99
Anything that degrades the signal
  E.g., resistance, power supply noise, coupling to neighboring wires, etc.
Example: a gate (driver) outputs 5 V but, because of resistance in a long wire, receiver gets 4.5 V
What is Noise?

## Slide 100
With logically valid inputs, every circuit element must produce logically valid outputs
Use limited ranges of voltages to represent discrete values
The Static Discipline

## Slide 101
Noise Margins

## Slide 102
High Noise Margin: NMH = VOH – VIH
Low Noise Margin: NML = VIL – VOL
Noise Margins

## Slide 103
Ideal Buffer: Real Buffer:
NMH = NML = VDD/2
DC Transfer Characteristics
NMH, NML < VDD/2

## Slide 104
DC Transfer Characteristics

## Slide 105
In 1970’s and 1980’s, VDD = 5 V
VDD has dropped
  Avoid frying tiny transistors
  Save power
3.3 V, 2.5 V, 1.8 V, 1.5 V, 1.2 V, 1.0 V, …
  Be careful connecting chips with different supply voltages
VDD Scaling

## Slide 106
In 1970’s and 1980’s, VDD = 5 V
VDD has dropped
  Avoid frying tiny transistors
  Save power
3.3 V, 2.5 V, 1.8 V, 1.5 V, 1.2 V, 1.0 V, …
  Be careful connecting chips with different supply voltages
Chips operate because they contain magic smoke
Proof: if the magic smoke is let out, the chip stops working
VDD Scaling

## Slide 107
Logic Family | VDD | VIL | VIH | VOL | VOH
TTL | 5 (4.75 - 5.25) | 0.8 | 2.0 | 0.4 | 2.4
CMOS | 5 (4.5 - 6) | 1.35 | 3.15 | 0.33 | 3.84
LVTTL | 3.3 (3 - 3.6) | 0.8 | 2.0 | 0.4 | 2.4
LVCMOS | 3.3 (3 - 3.6) | 0.9 | 1.8 | 0.36 | 2.7
Logic Family Examples

## Slide 108
Logic gates built from transistors
3-ported voltage-controlled switch
  2 ports connected depending on voltage of 3rd
  d and s are connected (ON) when g is 1
Transistors

## Slide 109
Nicknamed “Mayor of Silicon Valley”
Cofounded Fairchild Semiconductor in 1957
Cofounded Intel in 1968
Co-invented the integrated circuit
Robert Noyce, 1927-1990

## Slide 110
Transistors built from silicon, a semiconductor
Pure silicon is a poor conductor (no free charges)
Doped silicon is a good conductor (free charges)
  n-type (free negative charges, electrons)
  p-type (free positive charges, holes)
Silicon

## Slide 111
Metal oxide silicon (MOS) transistors:
  Polysilicon (used to be metal) gate
  Oxide (silicon dioxide) insulator
  Doped silicon
MOS Transistors

## Slide 112
Gate = 0
OFF (no connection between source and drain)
Gate = 1
ON (channel between source and drain)
Transistors: nMOS

## Slide 113
pMOS transistor is opposite
  ON when Gate = 0
  OFF when Gate = 1
Transistors: pMOS

## Slide 114
Transistor Function

## Slide 115
nMOS: pass good 0’s, so connect source to GND
pMOS: pass good 1’s, so connect source to VDD
Transistor Function

## Slide 116
A | P1 | N1 | Y
0 |  |  | 
1 |  |  | 
CMOS Gates: NOT Gate

## Slide 117
CMOS Gates: NOT Gate
A | P1 | N1 | Y
0 | ON | OFF | 1
1 | OFF | ON | 0

## Slide 118
A | B | P1 | P2 | N1 | N2 | Y
0 | 0 |  |  |  |  | 
0 | 1 |  |  |  |  | 
1 | 0 |  |  |  |  | 
1 | 1 |  |  |  |  | 
CMOS Gates: NAND Gate

## Slide 119
A | B | P1 | P2 | N1 | N2 | Y
0 | 0 | ON | ON | OFF | OFF | 1
0 | 1 | ON | OFF | OFF | ON | 1
1 | 0 | OFF | ON | ON | OFF | 1
1 | 1 | OFF | OFF | ON | ON | 0
CMOS Gates: NAND Gate

## Slide 120
CMOS Gate Structure

## Slide 121
How do you build a three-input NOR gate?
NOR Gate

## Slide 122
NOR3 Gate
How do you build a three-input NOR gate?

## Slide 123
How do you build a two-input AND gate?
Other CMOS Gates

## Slide 124
AND2 Gate
How do you build a two-input AND gate?
CMOS is better at building inverting gates (i.e., NAND, NOR, etc.)
I.e., a 2-input NAND gate requires 2 fewer transistors than a 2-input AND gate

## Slide 125
nMOS pass 1’s poorly
pMOS pass 0’s poorly
Transmission gate is a better switch
  passes both 0 and 1 well
When EN = 1, the switch is ON:
  EN = 0 and A is connected to B
When EN = 0, the switch is OFF:
  A is not connected to B
Transmission Gates

## Slide 126
Replace pull-up network with weak pMOS transistor that is always on
pMOS transistor: pulls output HIGH only when nMOS network not pulling it LOW
Pseudo-nMOS Gates

## Slide 127
Pseudo-nMOS NOR4
Pseudo-nMOS Example

## Slide 128
Cofounded Intel in 1968 with Robert Noyce.
Moore’s Law: number of transistors on a computer chip doubles every year (observed in 1965)
Since 1975, transistor counts have doubled every two years.
Gordon Moore, 1929-

## Slide 129
“If the automobile had followed the same development cycle as the computer, a Rolls-Royce would today cost $100, get one million miles to the gallon, and explode once a year . . .” (Robert Cringely, Infoworld)
– Robert Cringley
Moore’s Law

## Slide 130
Power = Energy consumed per unit time
Dynamic power consumption
Static power consumption
Power Consumption

## Slide 131
Power to charge transistor gate capacitances
  Energy required to charge a capacitance, C, to VDD is CVDD2
  Circuit running at frequency f: Transistors switch (from 1 to 0 or vice versa) at that frequency
  Capacitor is charged f/2 times per second (discharging from 1 to 0 is free)
Dynamic power consumption:
Pdynamic = ½CVDD2f
Dynamic Power Consumption

## Slide 132
Power consumed when no gates are switching
Caused by the quiescent supply current, IDD (also called the leakage current)
Static power consumption:
Pstatic = IDDVDD
Static Power Consumption

## Slide 133
Dynamic power + static power
Ptotal = Pstatic + Pdynamic
Total Power Consumption

## Slide 134
Estimate the power consumption of a wireless handheld computer
  VDD = 1.2 V
  C = 20 nF
  f = 1 GHz
  IDD = 20 mA
Power Consumption Example

## Slide 135
Estimate the power consumption of a wireless handheld computer
  VDD = 1.2 V
  C = 20 nF
  f = 1 GHz
  IDD = 20 mA
P = ½CVDD2f + IDDVDD
= ½(20 nF)(1.2 V)2(1 GHz) + (20 mA)(1.2 V)
= (14.4 + 0.024) W ≈ 14.4 W (14.424 W to be more exact)
Power Consumption Example